## Slide 1: Bradley Training and Assessment Course (BTAC) Student Read Ahead

## Slide 2
1.0 HP, 24 Vdc Motor Assembly
Small Bevel Gear
Large Bevel Gear
Clutch Assembly
Spur Gear Cluster
Spur Assembly Gear
Straight Drive Shaft
Drive Sprocket (Track Assembly)
(Receiver Assembly)
Lower Spur Gear
(Always)
Lower Sliding Sleeve Clutch
Lower Shouldered Shaft
Lower Feed Shaft Stop Assembly
Lower Feed Sprocket Assembly
Upper Sliding Sleeve Clutch
Upper Shouldered Shaft
Upper Feed Shaft Stop Assembly
Upper Feed Sprocket Assembly
Worm Shaft Assembly
Gear Clutch Assembly
(contains the gear for Manual drive, driven
By the Manual gear hub)
Worm Wheel Gear
Clutch Spur Gear (large gear)
Spur Gear shaft (Small Gear)
Upper Spur Gear
Control Cam
Bolt Position Indicator
Index Drive Shaft
Clutch Yoke Assembly
Actuator
Electrical Feed Select Solenoid
(contains a notch to hold Index Drive
Gears in precise alignment) Cam
Timing Cams
When Engaged
Rotor Stub
Feeder Assembly Rotor
E-1

## Slide 3
(
)
(
(
)
)
(
)
(
)
( )
(
)
E-1

## Slide 4: VERBATIM NOTE CARDS

## Slide 5: Forward Feed Section Subcomponents (Verbatim)
Round Positioner Assembly
Upper Feed Sprocket assembly
Feeder Assembly Rotor
Forward Feed Assembly
Lower Feed Sprocket Assembly
Ejection Chute

## Slide 6: Receiver Assembly Subassemblies (Verbatim)
Barrel support assembly
Recoil mechanism
Breech assembly
Sear assembly
Sear catch assembly
Sear retractor assembly
Mechanical safety interlock system
1.0 HP 24 VDC Motor assembly
Handle Pin
Electrical Sear Solenoid
Riveted Receiver assembly

## Slide 7: Firing Pin Assembly (Verbatim)
Fall is 0.56 inch (14.2 mm)
Protrudes through Bolt Face: 1.5mm to 2.5 mm
Firing pin strikes a M115 Percussion Primer
Delivers 32 inch-lbs
Requires 19 inch-lbs
Safety margin 13 inch-lbs

## Slide 8: 25-mm Equipment Data (Verbatim)
Time to rate: 0.15 sec, The delay from the time the gun receives the signal to start until mechanical actions begin to start.
Time to stop: 0.12 sec, The delay from the time the gun receives the signal to stop until mechanical actions begin to stop.

## Slide 9: 25-mm Equipment Data (Verbatim)
Power required: 1.0 HP 24 Vdc motor assembly
Voltage to Operate M242 Electrical System
Required: 18-28 VDC
Provided: 18-30 VDC
Average Used: 24 VDC
Safety Margin: 2 VDC
Rated at 28 VDC

## Slide 10: 25-mm Equipment Data (Verbatim)
Open Bolt Clearing Method: Cook-off safe
Absolute Hang-Fire Protection: Mechanical Safety Interlock System (MSIS)

## Slide 11: 25-mm Equipment Data (Verbatim)
Safety: Absolute Hang-Fire protection
(MSIS)
(Mechanical Safety Interlock System)

## Slide 12: 25-mm Equipment Data (Verbatim)
Peak Recoil Force: 12,000 pounds force (STD)
9,000 pounds force (ENH)

## Slide 13: 25-mm Equipment Data (Verbatim)
Reliability demonstrated: 22,000 (MRBF) (Mean Rounds Between Failure)

## Slide 14: 25-mm Equipment Data (Verbatim)
Dispersion: 0.5 mil
1000m – .5m off of center of aim 2000m – 1m off of center of aim

## Slide 15
Misfire: Total failure of a round to fire Hang-fire: Delay in the firing of a round
Cook-off: Accidental firing of a round due to excessive heat build up in the weapon system.
25-mm Equipment Data (Verbatim)

## Slide 16: Power Transmission System
1.0 HP 24 Vdc Motor Assembly
Feeder Drive Assembly
Chain and Bolt Drive
25-mm Equipment Data (Verbatim)

## Slide 17: Feed Dwell (Verbatim)
Bolt and carrier assembly is 25mm to the rear of Sear, its rearmost position.
The slider moves from left to right in the slider path
The Feeder assembly rotor will rotate 1/3 of a revolution (120 degrees)
This is happening to allow the feeder assembly rotor to sweep the spent casing into the ejection chute and place a new round on the face of the bolt assembly

## Slide 18: Fire Dwell (Verbatim)
Bolt assembly is locked in the breech assembly
The slider moves from right to left in the slider path
This is happening to allow hot propellant gases to escape returning chamber pressure to ambient (safe levels)

## Slide 19: Ramming/Extracting (Verbatim)
Positive round control is provided by the:
Positive T-slot extractors
Continuous rim guides

## Slide 20: Dual Feed System (Verbatim)
Link-aligners can move a long round 9.5mm back
Chamfered surface on the rear plate assembly can move a short round 3.1mm forward

## Slide 21: Double Feed Prevention (Verbatim)
The incoming round is positively prevented from feeding across into the ram position; the nose of the incoming round is ahead of the base of the round left in the chamber.
The positive T-slot extractors
Note: Based on M792/M793 ammo. The M791/M910/M919 with missing nose caps may allow a double feed situation to occur!

## Slide 22: Recoil Mechanism (Verbatim)
Two ring spring set
Hydraulic Damper
Absorbs 85% of recoil
Remaining 15% absorbed by vehicle
18 Inner (STD)
17 Outer (STD)
17 Inner (ENH)
16 Outer (EHN)

## Slide 23: Sear Assembly (Verbatim)
The primary purpose (function) of the sear assembly is to positively position the roller assembly chain master link, at the end of a firing burst, thereby orienting the gun components for feed selection.
The secondary purpose (Function) of the sear assembly, is to locate receiver assembly components, for proper timing of the feeder and receiver assemblies during assembly.

## Slide 24: Mechanical Safety Interlock System (Verbatim) 6 Components
Rocker assembly
Operating rod assembly
Push Rod Extension
Interlock Crank
Sear push rod
Sear assembly

## Slide 25: Mechanical Safety Interlock System Failure Modes (Verbatim)
Sear Assembly Breaks
Push Rod Extension or Externally Relieved Screw Breaks
Interlock Crank Breaks
Carrier Assembly Cam Breaks
Electrical Sear Solenoid Intermittent

## Slide 26: Timing of Power Train (Verbatim)
Two Timing requirements
Feeder housing disassembled
Feeder assembly removed from receiver assembly

## Slide 27: Electrical System (Verbatim)
Consists of 4 components
1.0 HP 24 VDC Motor assembly
Electrical Sear Solenoid
Electrical Feed Select Solenoid
Index Drive Cable assembly

## Slide 28: Index Drive Cable Assembly (Verbatim)
Electrical Feed Select Solenoid Wiring Harness
Micro Switch Sensor Harness Assembly

## Slide 29
IDENTIFY
Student Study Guide

## Slide 30: T-72
Grenade launchers on the R/S
Gunner’s night optics
22 round carousel auto-loader underneath crew compartment of turret
Gunner’s day optics
Brick shaped ERA
Single Driver periscope
7.62mm Coax
125mm MER: 3000m
AT-11 Sniper MER: 4000m
Engine exhaust on the L/S

## Slide 31: T-72
Skirts has 4 rows of Brick shaped ERA
6 evenly spaced road wheels
Rear sprocket drive and supported track
IR search light
No grenade launchers on right side
Bore evacuator 1/3 away from the end of muzzle
Vehicle commander on the R/S with 12.7mm MG
Brick shaped ERA
Single driver periscope
Extended range fuel tanks

## Slide 32: T-80
Add on armor & anti-armor RPG plates to protect turret ring
4 smoke grenade launchers on both sides
3 driver periscopes
Add-on armor plates front hull
Gunner’s night optics behind day optics
Gunner’s day optics
Vehicle commander on the R/S with 12.7mm MG
28 round carousel auto-loader underneath crew compartment of turret
7.62mm Coax
125mm MER: 3000m
AT-8 Songster MER: 4000m

## Slide 33: T-80
1 & 2 paired road wheels
3 & 4 paired road wheels
Supported track rear sprocket drive
Turbine engine exhaust center rear
125mm gun can fire a radio guided missiles.
Bore evacuator 1/3 from the end of the muzzle.
Add-on armor plates on front skirts
Anti-armor RPG plates to protect turret ring
Extended range fuel tank racks
Gunner’s day optics
Gunner’s night optics

## Slide 34: T-90
Gunner’s night optics
Gunner’s day optics
Vehicle commander on the R/S with 12.7mm MG
V-shaped cut add on armor around driver periscope
SHTORA optical jammer counter-measure vs. ATGMs
22 round carousel auto-loader underneath crew compartment of turret
Bulldozer blade
Laser warning receivers
7.62mm Coax
125mm MER: 3000m
AT-11b Sniper MER: 5000m

## Slide 35: T-90
6 evenly spaced road wheels
Rear sprocket drive and supported track
Engine exhaust on the L/S
3 segmented add-on armor plates on front skirts
KONTAKT 5 ERA on front turret shape of a wedge
125mm gun can fire a laser guided missile that can shoot down helicopters
SHTORA optical jammer counter-measure vs. ATGMs
V-shaped cut add on armor around driver periscope
Meteorological data collector

## Slide 36: BMP-2
Tube launch anti-tank guided missile
Speed boat shaped hull with trim vane
Front sprocket drive supported track
Gap between #4, 5, & 6 road wheel
Troop periscopes for the gun ports
Top of the track is high in relationship to the hull
Bullet deflectors
Two man larger turret shape of a fry pan
Muzzle break on the end
30mm MER: 1500m
AT-5 Spandrel MER: 4000m

## Slide 37: BMP-2
Bullet deflectors
Two man larger wide turret shape of a fry pan
30mm MER: 1500m
AT-5 Spandrel MER: 4000m
Skinny or thin tracks
Engine exhaust
Trim vane
IR search light

## Slide 38: BMP-3
Engine exhaust
Bow gunner hatch & 7.62mm MG
Bow gunner hatch & 7.62mm MG
Trim vane folds down
6 road wheels that have western style appearance
Two man flat wide turret shape of a fry pan
Driver center of hull
Vehicle commander
Gunner
Square rear end
30mm MER: 2000m
100mm HE & AT-10 Stabber MER: 4000m

## Slide 39: BMP-3
6 road wheels that have western style appearance
Rear sprocket drive supported track
Hydro propulsion system
Can carry 6 troops
Gunner’s optics
Square rear end

## Slide 40: BMD-2
5 road wheels that are evenly spaced
Rear sprocket drive supported track
4 track support rollers
Bullet deflectors in front of driver
30mm long skinny gun and tube launch ATGM
One man small turret for VC/Gunner
Bow gunner MG port
30mm MER: 1200m
AT-5 Spandrel MER: 4000m
Sloped rear end

## Slide 41: BMD-2
30mm long skinny gun and tube launch ATGM
Sloped rear end
Engine exhausts
Hydro propulsion system
Distinct truck bed appearance in the rear
One man small turret for VC/Gunner
5 road wheels that are evenly spaced
Rear sprocket drive supported track
4 track support rollers
Muzzle break on the end

## Slide 42: BMD-3
30mm long skinny gun
Squared rear end
Engine exhausts
Distinct truck bed appearance in the rear
Two man turret with a lower profile
5 road wheels that look like trash can lids
Rear sprocket drive supported track
4 track support rollers
Distinct duck bill front slope
30mm MER: 1200m
AT-5 Spandrel MER: 4000m

## Slide 43: BMD-3
30mm long skinny gun
Squared rear end
Two man turret with a lower profile
5 road wheels that look like trash can lids
Rear sprocket drive supported track
4 track support rollers
Distinct duck bill front slope and it’s straight edge
Trim vane folds on top
Tube launch ATGM
Driver center of hull

## Slide 44: BTR-70
Distinct sloped rear-end and exhaust
One man turret with no over head hatch
Troop step up in between #1 & 2 wheels
Distinct duck bill front slope and it’s straight edge. Trim vane folds on top
Troop exit door
14.5mm
MER: 2000m
Troop step up in between #3 & 4 wheels

## Slide 45: BTR-70
Distinct sloped rear-end and exhaust
One man turret with no over head hatch
Troop step up in between #1 & 2 wheels
Distinct duck bill front slope and it’s straight edge. Trim vane folds on top
Troop exit door
14.5mm MG
Troop step up in between #3 & 4 wheels
Twin eyelet windshields

## Slide 46: BTR-80
Exhaust rear-end is horizontally straight
One man turret with no over head hatch
Troop step up in between #1 & 2 wheels
Distinct duck bill front slope and it’s straight edge. Trim vane folds on top
Improved troop exit doors
Troop step up in between #3 & 4 wheels
14.5mm
MER: 2000m

## Slide 47: BTR-80
One man turret with no over head hatch
Troop step up in between #1 & 2 wheels
Distinct duck bill front slope and it’s straight edge. Trim vane folds on top
Improved troop exit doors
14.5mm MG
Troop step up in between #3 & 4 wheels
Twin eyelet windshields
Exhaust rear-end is horizontally straight

## Slide 48: TYPE 96
Rear sprocket drive supported track
6 road wheels with gap between #1, 2 & 3
Type 96 only has 2 engine exhausts on the R/S
ERA side turret
Both sides of the turret has 6 smoke grenade launchers
ERA front glacis
125mm gun with a bore evacuator 1/3 from the end of the muzzle
125mm MER: 3000m

## Slide 49: TYPE 96
125mm gun with a bore evacuator 1/3 from the end of the muzzle
ERA front glacis
Both sides of the turret has 6 smoke grenade launchers
6 road wheels with gap between #1, 2 & 3
ERA side turret
NO engine exhaust on L/S
ERA front slope
Driver sits on the L/S of hull
Gunner optics housing
Vehicle commander’s hatch
Meteorological data collector
Utilizes a T-72 design carousel auto-loader

## Slide 50: TYPE 99
Gunner optics housing smaller
Utilizes a T-72 design carousel auto-loader
125mm gun with a bore evacuator 1/3 from the end of the muzzle
Active high powered laser counter-measure vs. missiles
VC independent optics
Both sides of the turret has 5 smoke grenade launchers
ERA side turret
Driver sits center of the hull with 1 periscope
6 road wheels with #1 & 2 closely paired
Both sides has 1 engine exhausts
Distinct design of ERA on L/S of front glacis. Designed this way for driver exit clearance
ERA front slope
125mm MER: 3000m
AT-11b Sniper MER: 5000m

## Slide 51: TYPE 99
Gunner optics housing smaller
Utilizes a T-72 design carousel auto-loader
125mm gun with a bore evacuator 1/3 from the end of the muzzle
VC independent optics
Both sides of the turret has 5 smoke grenade launchers
Driver sits center of the hull with 1 periscope
6 road wheels with #1 & 2 closely paired
Both sides has 1 engine exhausts
ERA front slope
7.62mm Coax MG

## Slide 52: TYPE 97
Engine exhaust
Trim vane folds down
6 road wheels that has a gap between #4, 5, and 6
Two man flat wide turret shape of a fry pan
Driver center L/S of hull
Vehicle commander
Gunner optics
Front sprocket drive supported track
30mm MER: 2000m
100mm HE & AT-10 Stabber MER: 4000m

## Slide 53: TYPE 97
Front sprocket drive supported track
Hydro propulsion system
Troop exit door
6 road wheels that has a gap between #4, 5, and 6
Trim vane Up
Engine exhaust

## Slide 54: ZBL 09
30mm MER: 2000m
Red Arrow-8 MER: 4000m
Trim vane folds on top
Side view mirrors
Each wheel has an individual wheel well
Distinct hull gap separating the #2 & 3 wheels
Speed boat type front hull
Headlights

## Slide 55: ZBL 09
Side view mirrors
Propellers for amphibious operations
Troop exit door
Red Arrow-8 ATGM
30mm auto-cannon
Driver L/S of hull
Engine exhaust

## Slide 56: CHALLENGER 2
120mm MER: 4000m
with bore evacuator 1/3 from the end of the muzzle
Sharp angle front armor turret
VC independent viewer
Gap between #5 & 6 road with 6 sets of road wheels on both sides
Rear sprocket drive supported track
Engine exhaust on both sides of hull
Stowage boxes wrap around back of turret. Vertical side armor
Gunner thermal optics on gun mantle
Driver sits center of the hull

## Slide 57: CHALLENGER 2
Engine exhaust on both sides of hull
Sharp angle front armor turret
Gunner thermal optics on gun mantle
Gap between #5 & 6 road with 6 sets of road wheels on both sides
Rear sprocket drive supported track
Stowage boxes wrap around back of turret. Vertical side armor
120mm gun with bore evacuator 1/3 from the end of the muzzle

## Slide 58: WARRIOR
30mm MER: 1500m
Sharp sloped front end
Driver L/S of hull
VC & Gunner optics
Gap between #3 & 4 road wheels
Front sprocket drive supported track
Crew escape hatch

## Slide 59: WARRIOR
Front sprocket drive supported track
Engine exhaust R/S
Gap between #3 & 4 road wheels
Combat Identification Panel (CIP)
Sharp sloped front end
Rear stowage boxes are square

## Slide 60: LEOPARD 2
Leo 2A5 wedge shaped front armor
7 sets of road wheels evenly spaced
Rear sprocket drive supported track
120mm MER: 4000m
with bore evacuator 2/3 from the end of the muzzle
Driver’s hatch R/S of hull
Gunner’s optics housing

## Slide 61: LEOPARD 2
Leo 2A4 flat vertical front armor
7 sets of road wheels evenly spaced
Rear sprocket drive supported track
120mm gun with bore evacuator 2/3 from the end of the muzzle
Heater exhaust
Rear engine exhaust

## Slide 62: PUMA
Front sprocket drive supported track
Engine exhaust R/S
Gap between #3, 4 & 5 sets road wheels
VC independent optronic camera
Sharp sloped front end
Remote operated turret with 30mm MER: 3000m
Driver L/S of hull
Gunner optics
Non-amphibious IFV

## Slide 63: PUMA
Front sprocket drive supported track
Drop down troop ramp
Gap between #3, 4 & 5 sets of road wheels
VC independent optronic camera
Sharp sloped front end
Remote operated turret with 30mm cannon
Driver L/S of hull
Gunner optics
Non-amphibious IFV

## Slide 64: GTK BOXER
Remote operated, can be equipped with .50 cal or Grenade launcher
Modular crew compartment design. It can be removed from the wheel base.
8x8 wheeled APC distinct hull gap separating the #2 &3 wheels
VC hatch
Sharp sloped front end
12.7mm MER: 1800m
40mm MER: 2212m

## Slide 65: GTK BOXER
Modular crew compartment design. It can be removed from the wheel base.
8x8 wheeled APC distinct hull gap separating the #2 &3 wheels
.50 cal MG manually operated
Sharp sloped front end
Driver hatch has ballistic windshield when driving open hatch
Engine exhaust L/S
12.7mm MER: 1800m
40mm MER: 2212m

## Slide 66: LECLERC
Gunner R/S of turret with his optics
6 sets of road wheels evenly spaced
Rear sprocket drive supported track
120mm MER: 3000m
no bore evacuator segmented thermal shrouds
VC L/S of turret with an independent thermal camera
MRS collimator
Driver L/S of hull
Modular armor, designed to be unbolted and replaced if damaged in combat
Utilizes an auto-loader

## Slide 67: LECLERC
Engine exhaust L/R
Gunner R/S of turret with his optics
6 sets of road wheels evenly spaced
Rear sprocket drive supported track
120mm gun no bore evacuator segmented thermal shrouds
VC L/S of turret with an independent thermal camera
Driver L/S of hull
Modular armor, designed to be unbolted and replaced if damaged in combat
Utilizes an auto-loader

## Slide 68: VBCI
Modular armor designed to be unbolted and replaced if damaged in combat
8x8 wheeled APC with individual wheel wells for each wheel
DRAGAR one man turret that can be placed in automatic air defense mode using
25mm MER: 3000m chain gun
VC hatch L/S of hull
Driver hatch positioned on the down slope of the hull L/S
Rear smoke grenade launchers
Non-amphibious IFV

## Slide 69: VBCI
DRAGAR one man turret that can be placed in automatic air defense mode using 25mm chain gun & 7.62mm coax
Driver hatch positioned on the down slope of the hull L/S
VC hatch L/S of hull
Engine exhaust
Modular armor designed to be unbolted and replaced if damaged in combat
Bottom front end is shaped like a hammerhead shark
Rear smoke grenade launchers
Non-amphibious IFV

## Slide 70: K1A1
Turret lower silhouette in comparison to an Abrams
6 sets of road wheels on both sides
Rear sprocket drive supported track
120mm MER: 4000m
with bore evacuator 2/3 from the end of the muzzle
Vehicle commander on the R/S with an independent viewer
Driver’s L/S of the hull
Gunner’s optics housing
Smoke grenade launchers mounted in front of turret armor

## Slide 71: K1A1
Turret is tapered in the rear comparison to an Abrams
6 sets of road wheels on both sides #3 & 5 are paired together
Rear sprocket drive supported track
120mm gun with bore evacuator 2/3 from the end of the muzzle
Vehicle commander on the R/S of the turret
Driver’s L/S of the hull
2 rear diesel engine exhausts

## Slide 72: K21
Fully amphibious
40mm MER: 3000m
Sharp sloped front end
Driver L/S of hull
Gunner optics
6 sets of road wheels evenly spaced
Front sprocket drive supported track
2 ATGM launchers
VC independent viewer
Trim vane folds down from the bottom

## Slide 73: K21
Fully amphibious
40mm auto-cannon with cone muzzle break
Driver L/S of hull
Gunner optics
6 sets of road wheels evenly spaced
Front sprocket drive supported track
VC independent viewer
Drop down troop ramp door

## Slide 74: M1A1 ABRAMS
Angular large slab armored turret
Gap between #1 & 2 road with 7 sets of road wheels on both sides
Rear sprocket drive supported track
120mm MER: 4000m
with bore evacuator 2/3 from the end of the muzzle
Vehicle commander on the R/S with .50 CAL MG
Driver’s hatch center of hull
Gunner’s optics housing
Cylinder smoke grenade launchers indicate this is a Marine Abrams

## Slide 75: M1A1 ABRAMS
120mm gun with bore evacuator 2/3 from the end of the muzzle
Angular large slab armored turret
Gap between #1 & 2 road with 7 sets of road wheels on both sides
Rear sprocket drive supported track
Turbine rear engine exhaust
Bustle rack and stowage boxes
Combat Identification Panels (CIP)

## Slide 76: M2/M3 BRADLEY
VC independent viewer
Gunner’s optics housing
VC hatch
7.62mm Coax MG
Tow launchers in stowed position on L/S of turret
Driver’s hatch
25mm chain gun
Final drive housings
Engine exhaust
25mm MER: 2000m
TOW MER: 3750m

## Slide 77: M2/M3 BRADLEY
Front sprocket drive supported track
Gunner’s optics housing
Tow launchers in stowed position on L/S of turret
Driver’s hatch
25mm chain gun
Gap between #3 & 4 road wheels
Combat Identification Panel (CIP)

## Slide 78: LAV-25 COYOTE
Gunner’s optics housing
Trim vane
Driver L/S of hull
25mm MER: 2000m
Long continuous wheel well, no hull partitions
Muffler on R/S of hull only
Propellers on both rear ends of the hull
Turret is longer or turret overhang
Boat shape hull

## Slide 79: LAV-25 COYOTE
Propellers on both rear ends of the hull
25mm chain gun
Boat shape hull
Turret is longer or turret overhang
Long continuous wheel well, no hull partitions

## Slide 80: STRYKER (M1126 ICV)
Storage for tire changing equipment
Remote Weapon Station (RWS)
No propellers, non-amphibious vehicle
Winch
Driver L/S of hull
Slat/Bar armor standard feature in Iraq & Afghanistan
Inner ring in the wheel are troop step rings
VC hatch
Squad leader hatch
.50cal MER: 1800m
MK19 MER: 2212m

## Slide 81: STRYKER (M1126 ICV)
Engine exhaust
Slat/Bar armor standard feature in Iraq & Afghanistan
Remote Weapon Station (RWS)
Gap between #2 & 3 wheel
No propellers, non-amphibious vehicle
.50cal MER: 1800m
MK19 MER: 2212m

## Slide 82: AAV
Off-center from the hull is a one man turret with a dual trunnion axis .50 cal and MK 19
Driver L/S of hull
Enhanced Armor Appliqué Kit (EAAK)
.50cal MER: 1800m
MK19 MER: 2212m
Trim vane

## Slide 83: AAV
Enhanced Armor Appliqué Kit (EAAK)
Engine exhaust
6 sets of road wheels, gap between #3 & 4
Front sprocket drive un-supported track
Both sides of the rear- end have propellers
Off-center from the hull is a one man turret with a dual trunnion axis .50 cal and MK 19
.50cal MER: 1800m
MK19 MER: 2212m

## Slide 84: M-ATV
Front engine,
rear or 4-wheel drive, 4 passenger, 4 door truck
Variants shown will have a turret or CROW
.50cal MER: 1800m
MK19 MER: 2212m

## Slide 85: M-ATV
Variants shown will have a turret or CROW
Front engine,
rear or 4-wheel drive, 4 passenger, 4 door truck
.50cal MER: 1800m
MK19 MER: 2212m

## Slide 86
5 main rotor blades
Swept back wing weapon load mount points
Tail rotor is on the L/S
Bubble shaped tandem pilot canopies
Re-tractable landing gear
MI-24 HIND-D
12.7mm MER: 1500m
AT-2 Swatter 2500m

## Slide 87: MI-24P HIND-F
5 main rotor blades
Tail rotor is on the L/S
Bubble shaped tandem pilot canopies
Re-tractable landing gear
Large sloped wings to mount missiles & rockets
Twin air inlets
HIND-F has twin 30mm auto-cannons
Engine exhausts on both sides
Tail skid
Mid-air refueling stake

## Slide 88: MI-24P HIND-F
5 main rotor blades
Tail rotor is on the L/S
Bubble shaped tandem pilot canopies
Re-tractable landing gear
Large sloped wings to mount missiles & rockets
Twin air inlets
HIND-F has twin 30mm auto-cannons
Engine exhausts on both sides

## Slide 89: MI-28 HAVOC
5 main rotor blades
Under mount 30mm chain gun
Fixed wheeled landing gears
Engine exhausts on both sides of fuselage
Mouse nose radar
Armored angular shaped tandem pilot canopies
Stabilizer wing
30mm MER: 3000m
AT-6 Spiral MER: 5000m

## Slide 90: MI-28 HAVOC
Tail rotor is on the R/S
Mouse nose radar
Target sight system
High accuracy radar navigation system
Dual air inlets
Under mount 30mm chain gun
Fixed wheeled landing gears
Short sloped wing weapon load mount points
Stabilizer fin
Armored angular shaped tandem pilot canopies
30mm MER: 3000m
AT-6 Spiral MER: 5000m

## Slide 91: KA-52 HOKUM-B (Alligator)
Coaxial contra-rotating rotor blades
2 pilots sits next to each other in the canopy
Large airplane type nose to house the radar system
30mm chain gun mounted on the R/S fuselage
Re-tractable landing gears
Dual air inlets
No tail rotor
Vertical rudder
Weapon load mount wings are straight
Engine vector exhausts
30mm MER: 3000m
AT-9 Vikhr MER: 10,000m

## Slide 92: KA-52 HOKUM-B (Alligator)
Coaxial contra-rotating rotor blades
2 pilots sits next to each other in the canopy
Large airplane type nose to house the radar system
Re-tractable mid-air refueling stake
Re-tractable landing gears
Air inlet
Stabilizer fins
Weapon load mount wings are straight
No tail rotor
Vertical rudder
Engine exhausts on both sides of fuselage
30mm MER: 3000m
AT-9 Vikhr MER: 10,000m

## Slide 93: Z-10
Stabilizer wings
Target sight system
5 main rotor blades
Chin mount 30mm chain gun
Fixed wheeled landing gears
Short aerodynamic wing weapon load mount points
Tail rotor R/S
Angular shaped tandem pilot canopies
Engine exhausts on both sides of fuselage
30mm MER: 3000m
HJ-10 MER: 8000m

## Slide 94: Z-10
Stabilizer wings
Target sight system
5 main rotor blades
Chin mount 30mm chain gun
Fixed wheeled landing gears
Short aerodynamic wing weapon load mount points
Tail rotor R/S
Angular shaped tandem pilot canopies
Engine exhausts on both sides of fuselage
30mm MER: 3000m
HJ-10 MER: 8000m

## Slide 95: EC-665 TIGER
Tail rotor is on the R/S
4 main rotor blades
Mast mounted sight
Dual engine exhausts
Fixed wheeled landing gears
Short sloped wing weapon load mount points
Stabilizer wings
Angular shaped step tandem pilot canopies
30mm MER: 4000m
HOT MER: 4000m

## Slide 96: EC-665 TIGER
Tail rotor is on the R/S
4 main rotor blades
Target sight system
Air inlets
Dual engine exhausts
Fixed wheeled landing gears
Short sloped wing weapon load mount points
Stabilizer wings
Angular shaped step tandem pilot canopies
Chin mounted 30mm chain gun
30mm MER: 4000m
HOT MER: 4000m

## Slide 97: AH-64 APACHE
Target sight system
4 Main rotor blades
Fixed wheeled landing gears
Tandem pilot cockpit
Engine exhausts
Air inlets
Both sides of fuselage have straight wing weapon load mount points
Tail rotor L/S
Synchronized elevator wing
30mm chain gun
30mm MER: 4000m
Hellfire MER: 8000m

## Slide 98: AH-64 APACHE
Target sight system
4 Main rotor blades
Fixed wheeled landing gears
Tandem pilot cockpit
Engine exhausts
30mm chain gun
30mm MER: 4000m
Hellfire MER: 8000m

## Slide 99: AH-1 COBRA
2 or 4 main rotor blades depending on variant
Tail rotor L/S
Synchronized elevator wing
Fixed landing skids
Chin mounted 20mm Gatling gun
Tandem cockpit
Slim fuselage making it faster and harder to hit
Air inlets
Engine exhausts
20mm MER: 2000m
Hellfire MER: 8000m

## Slide 100: AH-1 COBRA
2 or 4 main rotor blades depending on variant
Fixed landing skids
Chin mounted 20mm Gatling gun
Tandem cockpit
Engine exhausts
20mm MER: 2000m
Hellfire MER: 8000m